## Slide 1: Software You’ll Need
OR
Install Mu:
https://codewith.mu/
Online Editor (with Chrome):
https://python.microbit.org/v/beta

## Slide 2: Hardware Drivers in MicroPython
CARLOS PEREIRA ATENCIO
Software Engineer @ .
@carlosperate

## Slide 3: Outline
Presentation:
  MicroPython
  How to drive hardware
  Communicating with other devices
  Hardware documentation
  Writing some code
  Debugging
Workshop!

## Slide 4: MicroPython
Lean and efficient Python 3 implementation
Can run in 16KBs RAM, 256KBs ROM
Includes parser, compiler and virtual machine
Small subset of the standard library
Available in a wide range of platforms

## Slide 5: MicroPython

## Slide 6: Finding A Driver
Adafruit CircuitPython mma8451 driver https://github.com/adafruit/Adafruit_CircuitPython_MMA8451/
Google is your friend
GitHub is your best friend
Use implementations in other languages as reference
Look for the official documentation
    Product page might contain additional documentation
    Google search part number
    Datasheets often found in random pages
    Look for the newest version

## Slide 7
How Does Code Move Electrons

## Slide 8: The Software Stack
Py Modules
Python code
MicroPython
Hardware Abstraction Layer
Microcontroller
I2C
SPI
ADC
DAC
I2S
SDIO
PWM
PDM
Ethernet
USB
CAN
RTC
Hardware
Software

## Slide 9: The Software-Hardware Stack
Py Modules
Python code
MicroPython
Hardware Abstraction Layer
Microcontroller
I2C
SPI
ADC
DAC
I2S
SDIO
PWM
PDM
Ethernet
USB
CAN
RTC
SD Card
Microphone
Speaker
Sensor
Analog sensor
Sensor
Audio Chip
Servo
Sensor
Sensor
Hardware
Software

## Slide 10: Memory Map And Peripherals

## Slide 11: Memory Map And Peripherals

## Slide 12: Registers

## Slide 13: Registers

## Slide 14: Registers

## Slide 15: Registers

## Slide 16
Talking With Other Electronic Devices

## Slide 17: Talking With Electronic Devices
Some devices use analog signals as inputs or outputs
    Analog sensors encode simple data in the voltage magnitude
    Optic fibre modulates data using multiple techniques
Most electronic components in a PCB use digital signals
Data is sent in serial/parallel communication protocols
We’ll cover the most common digital protocols

## Slide 18: I²C Protocol
...
Slave
Slave
Slave
Master
SDA SCL
VDD
Inter-Integrated Circuit
Synchronous serial protocol
1 clock signal, 1 data signal
Single master, multiple slaves
  Multi-master possible
All sharing the same bus
Each slave has individual address
Commonly at 100 KHz or 400 KHz
  sometimes higher speeds available
SMB based on I2C

## Slide 19: I²C Protocol
Protocol diagram from: https://rheingoldheavy.com/i2c-signals/
from microbit import i2c
i2c.write(SLAVE_ADDRESS, bytes([DATA…]), repeat=True) data = i2c.read(SLAVE_ADDRESS, NUMBER_OF_BYTES)

## Slide 20: How do we know what to send down the wire?
Datasheets!

## Slide 21
Putting Things
Together

## Slide 22: Example Driver Initialisation

## Slide 23: Example Driver Initialisation

## Slide 24: Example Driver Initialisation

## Slide 25: Example Driver Initialisation

## Slide 26: Example Driver Initialisation

## Slide 27: Code Tips
For constant values use const() for compiler optimisation
ustruct very useful to pack/unpack blocks of data to/from variables
Bitwise operations (>> << & | ^ ~) to target bits in registers
Need to be careful about memory allocation (including temp ones!)
Buffer preallocation for driver read data is more efficient
The gc and micropython modules can be used to control collection and profile memory
Documentation
  http://docs.micropython.org/en/latest/reference/speed_python.html
  http://docs.micropython.org/en/latest/reference/constrained.html

## Slide 28
What if Something Goes Wrong?

## Slide 29: Debugging 🐛
Check all connections and power supply
Double check all connections and power supply
Make sure all devices share ground
Make sure all devices have same logic level (5V vs 3.3V)
Reduce the data transfer speed
Find the simplest possible code example to replicate your issue
Search for application notes and other implementations
Search for erratas

## Slide 30: Debugging 🐛
Capture and retrieve the data sent and received
Print debug
Hardware debuggers
  SEGGER J-Link EDU Mini
  Black Magic Probe
  Some development boards have integrated debuggers
    DAPLink, ST-Link, J-Link
Logic analyser
LEDs

## Slide 31: Logic Analysers
Saleale is a nice entry level professional tool
SigRok (with PulseView) is an open source signal analysis software
  Low cost SigRok-compatible devices start at £10

## Slide 32
Let’s get coding!
https://github.com/carlosperate/micropython-driver-workshop
OR https://git.io/Je3tM

## Slide 33: BBC micro:bit
User buttons
5x5 LED Matrix
Edge Connector

## Slide 34: BBC micro:bit
Battery connector
Magnetometer
16 MHz Cortex-M0+
Bluetooth
Reset Button
Micro USB
Acceleromater
2.4GHz Antenna

## Slide 35: Code Tips 29 == 0x1D
For constant values use micropython.const() for compiler optimisation
  VARIABLE = const(0x55)
Creating a “buffer” (to send via I2C):
  bytes([DATA_LIST])
ustruct very useful to pack/unpack blocks of data to/from variables
  output_tuple = ustruct.unpack('b', b'\x55’)
  https://docs.micropython.org/en/latest/library/ustruct.html
Bitwise operations (>> << & | ^ ~) to target bits in registers
  Shit a bit 3 places to the left: result = 1 << 3
  Set bit 3: result = original | (1 << 3)
  Flip all bits: 0b11110111 = ~0b00001000
  Clear bit 3: result = original & ~(1 << 3)
  https://wiki.python.org/moin/BitwiseOperators